## Slide 1
Manfred Kaltenbacher and Andreas Hüppe
Institute of Mechanics and Mechatronics, Vienna University of Technology
Austria
Coupled Field Simulation

## Slide 2: Outline
Overview about CFS++
  History
  Capabilities
  General Approach
Preprocessing
  ANSYS (Classic), Gmsh, ...
  Physical definitions
  Material definition
Performing simulation
  Simulation parameters
Postprocessing
  Result files
  ParaView

## Slide 3: CFS++: History
In the beginning
  M. Kaltenbacher and PhD students at Department of Sensor Technology, Friedrich-Alexander University (FAU) Erlangen-Nuremberg, year 2000
Currently involved groups
  Kaltenbacher‘s group
    Institute of Mechanics and Mechatronics, Vienna University of Technology
  R. Lerch‘s group
    Department of Sensor Technology, Friedrich-Alexander University Erlangen-Nuremberg
  M. Stingl‘s group
    Chair of Applied Mathematics 2, Friedrich-Alexander University Erlangen-Nuremberg

## Slide 4: History: People
Co-operation partners
  S. Reitzinger (support in the design phase)
  M. Hofer (bilinear and linear forms)
  M. Mohr (algebraic system and XML-structure)
  T. Lahmer (inverse schemes)
  B. Schmidt (contact handling)
Former Ph.D. students
  E. Zhelezina (first implementations)
  M. Escobar (aeroacoustics)
  G. Link (fluid flow and coupling to mechanics)
Current Ph.D. students
  A. Hauck (revisions of class structure, p-FEM, gFEM)
  J. Grabinger (non-matching grids, aeroacoustics)
  S. Zörner (fluid-structure-acoustic)
  A. Volk (magnetostriction)
Post Docs and others
  A. Hüppe (aeroacoustics, spectral-FEM, mixed FEM, revisions of class structure)
  M. Kaltenbacher (nonlinear PDEs, moving mesh, material modeling, hysteresis )
  S. Triebenbacher (non-matching grids, aeroacoustics, CFSDEPS, CMake)
  F. Wein (optimization)
Refer to contributors section in developer’s manual

## Slide 5: CFS++ Capabilities
Capabilities
  Single Field:
    Electromagnetics
    Mechanics
    Acoustics
    Flow
  FE Topics
    Finite Element of higher order (pFEM, spectral FEM)
    Non-conforming grids
    Moving meshes
    Material models with hysteresis
    Micro-Macro Modeling (Homogenization)
    Fast solvers (AMG, Pardiso)
    Optimization (SIMP, topology, shape)
    Inverse schemes (material parameter determination)
Multi-Field
  Piezoelectricity
  Electrostatics-Mechanics-Acoustics
  Magnetic-Mechanics-Acoustics
  Flow-Mechanics-Acoustics
Commercial version NACS
  Highly optimized
  Professional support by SiMetris
  GmbH Tennenlohe, Germany

## Slide 6: CFS++ Capabilities
CMUTs
Piezoelectric US-array
Electrodynamic loudspeaker
Piezoelectric stack
Electromagnetic valve
MRI-Scanner
Flow-induced sound
Transformer noise

## Slide 7: Literature
M. Kaltenbacher: Numerical Simulation of Mechatronic Sensors and Actuators, 2nd Edition, Springer 2007, 2nd edition
M. Kaltenbacher: Advanced Simulation Tool for the Design of Sensors and Actuator. Proceeding of Eurosensors XXIV 2010
Just search for scientific articles
  Andreas Hauck
  Andreas Hüppe
  Jens Grabinger
  Tom Lahmer
  Gerhard Link
  Manfred Kaltenbacher
  Simon Triebenbacher
  Adiran Volk
  Fabian Wein
  Stefan Zörner
  …………..

## Slide 8: Copyright
Overview
  No license file exists!
  CFS++ is considered open source as it has been developed, and is still developed by projects funded by public research agencies!
Gentleman’s agreement
  CFS++ shall not be publicly available
  Manfred Kaltenbacher is informed prior to distribution
  Development server (SVN, Trac, etc.) in Erlangen
  Development approach
    Everybody works on own branches
    Test cases prevent side effects
    Not everything ends on the trunk
trunk
task 1
task 2
branch
branch
merge
merge
time
revision 1
r. 2
r. 3
r. 4
r. 5
r. 6
r. 7
r. 8
r. 9
r. 10
r. 11

## Slide 9: CFS++ - Schema
Model: mesh data
Problem: XML file defining problem and physical properties
CFS++: command line based FEM solver/ optimizer
Postprocessing: visualization and calculations
Text: detailed information in ASCII, CSV or XML format
Preprocessing
(e.g. ANSYS, Gmsh,
GiD, COMSOL, etc.)
Postprocessing
(e.g. ParaView, GiD,
Matlab, Python, etc.)
Model
Problem
Text
Postprocessing
CFS++

## Slide 10: CFS++: General Approach
CFS++ (Coupled Field Simulation):
  Models: Based on partial differential equations (PDEs)
  Solution of PDEs: Finite-Element-Method
  Example: Structure for piezoelectric-acoustic coupled PDEs

## Slide 11: CFS++: General Approach
CFS++ (Coupled Field Simulation):
  Models: Based on partial differential equations (PDEs)
  Solution of PDEs: Finite-Element-Method
  Example: Structure for piezoelectric-acoustic coupled PDEs

## Slide 12: CFS++: General Approach
CFS++ (Coupled Field Simulation):
  Coupling: Electrostatics-Mechanics-Acoustics (MEMS)
Iter
ElecMech
-Linearform
ElecForce
LinearForm
+CalcElementVector()

## Slide 13: CFS++: General Approach
CFS++ (Coupled Field Simulation):
  Coupling: Electrostatics-Mechanics-Acoustics (MEMS)

## Slide 14: CFS++: General Approach
CFS++ (Coupled Field Simulation):
  Coupling: Electrostatics-Mechanics-Acoustics (MEMS)

## Slide 15: CFS++: General Approach
Pre-processing
  Supported pre-processors: ANSYS (Workbench), GiD, Gmsh, COMSOL, etc…
Physical problem description in XML format:
Post-processing
  Supported post-processors: ParaView, GiD, Gmsh, GMV, EnSight, Tecplot, ANSYS ,…
  Coordinates and mesh topology of all 3D (volume), 2D (surface) and 1D (interface) elements
<couplingList> <direct> <piezoDirect> <regionList> <region name="solid"/> </regionList> </piezoDirect> … | … <acouMechDirect> <surfRegionList> <surfRegion name="interface"/> </surfRegionList> </acouMechDirect> </direct> </couplingList>

## Slide 16: Example 1: Mechanics
Problem setup
  Cantilever with pressure load
Goal
  Perform
    Static analysis
    Transient analysis
    Harmonic analysis
    Eigenfrequency analysis
Fully supported
Pressure load (100N/m2)

## Slide 17: Example 1: Mechanics
Preprocessor: ANSYS Classic using prep7 commands
  Initialization part
  Define constants and generate geometry
fini /uis,msgpop,3 ! disable warning popups /clear /filname,cantilever,1 ! important: define name of the model /prep7 /uis,msgpop,2 ! enable warning popups init ! initialize macros for mesh-interface to CFS++
! define constants eps=1e-7 L=400e-6 b=2e-6 bc=45e-6 ! generate the cantilever block,0,L,0,bc,0,b

## Slide 18: Example 1: Mechanics
Preprocessor: ANSYS Classic using prep7 commands
  Perform volume meshing
  Perform surface mesh for pressure load and mechanical fixing
setelems,'brick' esize,5e-6 vsel,s,,,1 vmesh,all
setelems,'quadr' allsel asel,s,,,2 amesh,all allsel asel,s,loc,x,-eps,eps asel,r,loc,y,-eps,bc+eps asel,r,loc,z,-eps,eps+b amesh,all

## Slide 19: Example 1: Mechanics
Preprocessor: ANSYS Classic using prep7 commands
  Display of mesh

## Slide 20: Example 1: Mechanics
Preprocessor: ANSYS Classic using prep7 commands
  Write mesh file for CFS++: Write volume elements
  Write mesh file for CFS++: Write surface elements
allsel,all vsel,s,,,1 eslv welems,'cantilever'
! write surface elements for pressure load allsel asel,s,,,2 esla welems,'excite' ! write surface elements for mechanical fixing allsel asel,s,loc,x,-eps,eps asel,r,loc,y,-eps,bc+eps asel,r,loc,z,-eps,eps+b+b esla welems,'fix-all'

## Slide 21: Example 1: Mechanics
Write mesh file for CFS++
  Write mesh file for CFS++: Write coordinates of nodes
  Write mesh file for CFS++: Write the whole HDF5 file
  Result
    Within this directory you should now find the file cantilever.h5!
Problems:
  If there are inconsistencies, then you will get the error „MKHDF5: Please check the contents of cantilever_cplreader.out”.
! write all nodes allsel wnodes
! write mesh file in HDF5 format mkhdf5

## Slide 22: Example 1: Mechanics
Look at contents of mesh file using HDFView (http://www.hdfgroup.org/HDF5)
Hierarchical
structure for
mesh and results
Datasets for element
connectivities
and types
Dataset for node
coordinates
Datasets for
specifying which
elements and nodes
belong to which
region

## Slide 23: Example 1: Mechanics
Setup the XML file for describing the physics and simulation parameter
  Use <oXygen/> XML editor (see http://www.oxygenxml.com/)
  Associate W3C XML schema for CFS++ simulations

## Slide 24: Example 1: Mechanics
Setup the XML file for describing the physics and simulation parameter
  Hint: search for a similar problem in the CFS++ - TESTSUIT
  Header
  File section
<cfsSimulation xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:schemaLocation="http://www.cfs++.org ../CFS/share/xml/CFS-Simulation/Schemas/CFS_FileFormats.xsd xmlns="http://www.cfs++.org">
<fileFormats> <input> <hdf5 fileName="cantilever.h5"/> </input> <output> <text/> <hdf5/> </output> <materialData file="mat.xml"/> </fileFormats>

## Slide 25: Example 1: Mechanics
<domain geometryType="3d"> <regionList> <region material="Steel" name="cantilever"/> </regionList> <surfRegionList> <surfRegion name="excite"/> <surfRegion name="fix-all"/> </surfRegionList> <nodeList> <nodes name="record"> <!– Find the mesh node next to coordinate and assign the name "record" to it --> <coord x="400e-6" y="0" z="0"/> </nodes> </nodeList> </domain>
Setup the XML file for describing the physics and simulation parameter
  Define computational domain with volume-regions, surface-regions, ..
Define a new node for data recording

## Slide 26: Example 1: Mechanics
Setup the XML file for describing the physics and simulation parameter
  Start the sequence and define the analysis type
  Define the partial differential equation (PDE) and the region it is defined
<sequenceStep> <analysis> <static/> </analysis>
<pdeList> <mechanic subType="3d"> <regionList> <region name="cantilever"/> </regionList>

## Slide 27: Example 1: Mechanics
Setup the XML file for describing the physics and simulation parameter
  Define boundary conditions
  Define store results
<bcsAndLoads> <pressure name="excite" value="100"/> <fix name="fix-all"> <comp dof="x"/> <comp dof="y"/> <comp dof="z"/> </fix> </bcsAndLoads>
<storeResults> <nodeResult type="mechDisplacement"> <allRegions/> <nodeList> <nodes name="record"/> </nodeList> </nodeResult> </storeResults>

## Slide 28: Example 1: Mechanics
Setup the XML file for describing the physics and simulation parameter
  Close PDE part
  Define solver (not necessary)
  Close the sequence and the whole xml-definition
</mechanic> </pdeList>
<linearSystems> <system> <solverList> <pardiso/> </solverList> </system> </linearSystems>
</sequenceStep> </cfsSimulation>

## Slide 29: Example 1: Mechanics
Setup the XML file for the material parameters
<?xml version="1.0"?> <cfsMaterialDataBase xmlns="http://www.cfs++.org"> <material name="Steel"> <mechanical> <density> 7.8E03 </density> <elasticity> <isotropic> <real> <elasticityModulus> 210E09 </elasticityModulus> <poissonNumber> 0.3 </poissonNumber> </real> </isotropic> </elasticity> </mechanical> </material> </cfsMaterialDataBase>

## Slide 30: Example 1: Mechanics
Perform the simulation with CFS++
  Just „cfs“ you get the follwoing help (provided that the executable is in the path)

## Slide 31: Example 1: Mechanics
Perform the simulation with CFS++
  Type in „cfs cantileverStatic“ and you obtain
  Generated output files
    In results_hdf5: cantileverStatic.h5: contains the simulation result
    In history: cantileverStatic-ms1-mechDisplacement-node-91-record.hist
    In current directory: cantileverStatic.info.xml

## Slide 32: Example 1: Mechanics
Perform postprocessing with ParaView (http://www.paraview.org/)
  Start „paraview“ and display the result

## Slide 33: Example 1: Mechanics
<bcsAndLoads> <pressure name="excite“ value="100*sin(2*pi*1*t)" />
Perform a transient analysis
  Change analysis part
  Change in „bcsAndLoads“ for pressure excitation
Frequency of 1Hz
<sequenceStep> <analysis> <transient> <numSteps> 40 </numSteps> <deltaT> 0.05 </deltaT> </transient> </analysis>

## Slide 34: Example 1: Mechanics
Perform a harmonic analysis
  Change analysis type
  Change pressure load towards amplitude and phase
<bcsAndLoads> <pressure name="excite“ value="100" phase="0.0" />
<sequenceStep> <analysis> <harmonic> <numFreq> 10 </numFreq> <startFreq> 10 </startFreq> <stopFreq> 1e4 </stopFreq> <sampling>linear</sampling> </harmonic> </analysis>

## Slide 35: Example 1: Mechanics
Perform an eigenfrequency analysis
  Change analysis type
  No load is needed (not necessarly be changed)
<bcsAndLoads> <fix name="fix-all"> <comp dof="x"/> <comp dof="y"/> <comp dof="z"/> </fix> </bcsAndLoads>
<sequenceStep> <analysis> <eigenFrequency> <isQuadratic> no </isQuadratic> <numModes> 5 </numModes> <freqShift> 0 </freqShift> <writeModes> yes </writeModes> </eigenFrequency> </analysis>

## Slide 36: Example 1: Mechanics
Perform the simulation with CFS++
  Type in „cfs cantileverEigenfrequency“ and you obtain

## Slide 37: Example 2: Acoustics
Problem setup: wave propagation with sound barrier (point source excitation)

## Slide 38: Example 2: Acoustics
Preprocessor: Gmsh (http://geuz.org/gmsh)

## Slide 39: Example 2: Acoustics
Define constants
Bottom up modeling approach for structured mesh:
  Points → lines → surfaces → volumes → mesh
overall = 10; pmlW = 1; plateW = 0.1; plateH = 3.5; platePosX = 2; platePosY = 2.25; elemSize = 0.1;
//define basepoint for plate basePoint = -overall/2+pmlW+platePosY; Point(1) = {-overall/2, -overall/2 , 0, 1.0}; Point(2) = {-overall/2, -overall/2+pmlW , 0, 1.0}; Point(3) = {-overall/2, basePoint , 0, 1.0}; Point(4) = {-overall/2, basePoint+plateH , 0, 1.0}; Point(5) = {-overall/2, overall/2-pmlW , 0, 1.0}; Point(6) = {-overall/2, overall/2 , 0, 1.0};

## Slide 40: Example 2: Acoustics
Define lines
Current state
Line(1) = {1, 2}; Line(2) = {2, 3}; Line(3) = {3, 4}; Line(4) = {4, 5}; Line(5) = {5, 6};

## Slide 41: Example 2: Acoustics
Extrusion leads to mis-oriented elements but CFS++ will correct this later on
Get rid of multiple entities
Extrude{ pmlW, 0, 0 }{ Line{1,2,3,4,5}; } Extrude{ platePosX, 0, 0 }{ Line{6,10,14,18,22}; } Extrude{ plateW, 0, 0 }{ Line{26,30,34,38,42}; } Extrude{ overall-2*pmlW-platePosX-plateW, 0, 0 }{ Line{46,50,54,58,62}; } Extrude{ pmlW, 0, 0 }{ Line{66,70,74,78,82}; }
//combine double entities Coherence;

## Slide 42: Example 2: Acoustics
Generate regions to address later in CFS++
Structured meshing and recombine triangles to quadrilaterals
Physical Surface("prop") = {33,53,73,38,77,41,61,81,37}; Physical Surface("plate") = {57}; Physical Surface("pml") = { 9,29,49,69,89,93,97,101,105,85,65,45,25,21,17,13 };
Transfinite Surface '*'; Recombine Surface '*'; Transfinite Line {7,8,12,16,20,24,87,88,92,96,100,104} = ((pmlW)/elemSize) Using Progression 1; Transfinite Line {27,28,32,36,40,44} = ((platePosX)/elemSize) Using Progression 1; Transfinite Line {47,48,52,56,60,64} = ((plateW)/elemSize) Using Progression 1; Transfinite Line {67,68,72,76,80,84} = ((overall-2*pmlW-platePosX-plateW)/elemSize) Using Progression 1; …

## Slide 43: Example 2: Acoustics
Perform meshing with 2nd order elements
Color by physical entities
  Tools → Options → Mesh
    Visibility → Surface faces
    Color → Coloring mode
    → By physical group
Save the mesh file
  From GUI:
    File → Save Mesh
    Modules → Mesh → Save
  From command line:
$ gmsh -2 -bin -n -nopopup plateMesh.geo
Mesh.ElementOrder = 2; Mesh.SecondOrderIncomplete = 1; Mesh 2;
prop
plate
pml

## Slide 44: Example 2: Acoustics
Setup the XML file for describing the physics and simulation parameter (just will discuss differences to previous example)
  Hint: search for a similar problem in the CFS++ - TESTSUIT
  Domain with regions
<domain geometryType="plane"> <regionList> <region material="air" name="prop"/> <region material="air" name="plate"/> <region material="air" name="pml"/> </regionList> <nodeList> <nodes name="excite"> <coord x="0.0" y="0.0" z="0.0"/> </nodes> </nodeList> </domain>
Define excitation node.
One could also define
a Physical Point in Gmsh.

## Slide 45: Example 2: Acoustics
Setup the xml-File for describing the physics and simulation parameter
  Start the sequence and define analysis
  Define PDE for acoustics
<pdeList> <acoustic> <regionList> <region name="prop"/> <region name="pml" dampingId="myPml"/> </regionList>
<sequenceStep> <analysis> <harmonic> <numFreq> 10 </numFreq> <startFreq> 0.1 </startFreq> <stopFreq> 2 </stopFreq> <sampling>linear</sampling> </harmonic> </analysis>

## Slide 46: Example 2: Acoustics
Setup the xml-File for describing the physics and simulation parameter
  Define the PML (Perfectly Matched Layer) used for free field radiation
  Define excitation and output results
<bcsAndLoads> <pressure value="1" name="excite"/> </bcsAndLoads> <storeResults> <nodeResult type="acouPressure"> <allRegions/> </nodeResult> </storeResults>
<dampingList> <pml id="myPml"> <type> inverseDist </type> <dampFactor>1.0</dampFactor> </pml> </dampingList>

## Slide 47: Example 2: Acoustics
Material file
  Speed of sound
<cfsMaterialDataBase xmlns="http://www.cfs++.org"> <material name="air"> <acoustic> <density> 1 </density> <compressionModulus> 1 </compressionModulus> </acoustic> </material> </cfsMaterialDataBase>

## Slide 48: Example 2: Acoustics
Perform simulation „cfs noiseBarrier“ and start ParaView to investigate the solution
0.31Hz
2Hz

## Slide 49: Example 3: Piezoelectricity
Problem setup: Steel cantilever and piezoelectric layer (bimorph)
Goal
  Perform a static analysis to obtain deflection, mechanical stresses and electric field intensity
Fully supported
Steel cantilever
Piezoelectric layer
Ground
electrode
Hot electrode

## Slide 50: Example 3: Piezoelectricity
setelems,'quadr' allsel, asel,s,,,2 asel,a,,,5 asel,a,,,8 asel,a,,,11 amesh,all
block,0,L,0,bc,0,b block,0,L,0,bc,b,2*b nummrg,all,1e-7
Preprocessor: ANSYS Classic using prep7 commands (just addition parts, which are different to example 1)
  Generate volume for steel cantilever and piezoelectric layer
  Perform surface meshing for both electrodes (ground and loaded electrode) and for the surface, where the structure is mechanically fixed.
Cleans the model from doubled
keypoints, lines, areas, …

## Slide 51: Example 3: Piezoelectricity
Preprocessor: ANSYS Classic using prep7 commands
  Write volume elements for both cantilever and piezoelectric layer
  Write surface elements for mechanical fixing and electrodes
allsel asel,s,,,2 esla welems,'gnd' | allsel asel,s,,,2 esla welems,'gnd' | allsel asel,s,,,5 asel,a,,,11 esla,,1 welems,'fix-all'
allsel,all vsel,s,,,1 eslv welems,'cantilever' allsel,all vsel,s,,,2 eslv welems,'piezoLayer'

## Slide 52: Example 3: Piezoelectricity
Setup the XML file for describing the physics and simulation parameter (just will discuss differences to previous examples)
  Domain with regions
<domain geometryType="3d"> <regionList> <region name="cantilever" material="Steel"/> <region name="piezoLayer" material="PZT-5H"/> </regionList> <surfRegionList> <surfRegion name="gnd"/> <surfRegion name="top"/> <surfRegion name="fix-all"/> </surfRegionList>

## Slide 53: Example 3: Piezoelectricity
Setup the XML file for describing the physics and simulation parameter
  Mechanical PDE
  Electrostatic PDE
<pdeList> <mechanic subType="3d"> <regionList> <region name="cantilever"/> <region name="piezoLayer"/> </regionList> …
… <electrostatic> <regionList> <region name="piezoLayer"/> </regionList> <bcsAndLoads> <ground name="gnd"/> <potential value="1.0" name="top"/> </bcsAndLoads> …

## Slide 54: Example 3: Piezoelectricity
Setup the XML file for describing the physics and simulation parameter
  Coupling section
Let’s run by typing „cfs bimorph“ and analyze the results by using ParaView
<couplingList> <direct> <piezoDirect> <regionList> <region name="piezoLayer"/> </regionList> </piezoDirect> </direct> </couplingList>

## Slide 55: Example 3: Piezoelectricity
For more details
  Advanced Pre- and Postprocessing manual
  XML-Reference manual
  Introduction to Modeling and Simulation with CFS++
  Look up the examples in the TESTSUIT